## Slide 1: Efficient Processing of Deep Neural Networks: from Algorithms to Hardware Architectures
@eems_mit)
1
Vivienne Sze Massachusetts Institute of Technology
In collaboration with
Tien-Ju Yang, Yu-Hsin Chen, Joel Emer
Slides available at https://tinyurl.com/SzeNeurIPS2019

## Slide 2: Compute Demands for Deep Neural Networks
[Strubell, ACL 2019]
Year
Source: Open AI (https://openai.com/blog/ai-and-compute/)
AlexNet to AlphaGo Zero:
A 300,000x Increase in Compute
Petaflop/s-days (exponential)
@eems_mit)
2

## Slide 3: Processing at the “Edge” instead of the “Cloud”
Communication
Privacy
Latency
@eems_mit)
3

## Slide 4: Deep Neural Networks for Self-Driving Cars
(Feb 2018)
Cameras and radar generate ~6 gigabytes of data every 30 seconds.
Prototypes use around 2,500 Watts.
Generates wasted heat and some prototypes need water-cooling!
@eems_mit)
4

## Slide 5: Existing Processors Consume Too Much Power
< 1 Watt
@eems_mit)
5
> 10 Watts

## Slide 6: Transistors Are Not Getting More Efficient
Slowdown of Moore’s Law and Dennard Scaling General purpose microprocessors not getting faster or more efficient
Slowdown
@eems_mit)
6
Need specialized / domain-specific hardware for significant improvements in
speed and energy efficiency

## Slide 7: Goals of this Tutorial
Image Source: [Dean, ISSCC 2020]
Moore’s Law
 Many approaches for efficient processing of DNNs. Too many to cover!
Number of DNN processor papers at top-tier hardware conferences
Artificial Intelligence
Machine Learning Brain-Inspired
Spiking
Neural Networks
Deep Learning
@eems_mit)
7
Image Source: [Sze, PIEEE 2017]

## Slide 8: Goals of this Tutorial
Artificial Intelligence
Machine Learning Brain-Inspired
Spiking Neural Networks
Deep Learning
Image Source: [Sze, PIEEE 2017]
 Many approaches for efficient processing of DNNs. Too many to cover!
Big Bets On A.I. Open a New Frontier for Chips Start-Ups, Too. (January 14, 2018)
“Today, at least 45 start-ups are working on chips that can power tasks like speech and self-driving cars, and at least five of them have raised more than $100 million from investors. Venture capitalists invested more than $1.5 billion in chip start-ups last year, nearly doubling the investments made two years ago, according to the research firm CB Insights.”
@eems_mit)
8

## Slide 9: Goals of this Tutorial
@eems_mit)
9
Many approaches for efficient processing of DNNs. Too many to cover!
We will focus on how to evaluate approaches for efficient processing of DNNs
  Approaches include the design of DNN hardware processors and DNN models
  What are the key questions to ask?
Specifically, we will discuss
  What are the key metrics that should be measured and compared?
  What are the challenges towards achieving these metrics?
  What are the design considerations and tradeoffs?
We will focus on inference, but many concepts covered also apply to training

## Slide 10: Tutorial Overview
@eems_mit)
10
Deep Neural Networks Overview (Terminology)
Key Metrics and Design Objectives
Design Considerations
  CPU and GPU Platforms
  Specialized / Domain-Specific Hardware (ASICs)
  Break Q&A
  Algorithm (DNN Model) and Hardware Co-Design
  Other Platforms
Tools for Systematic Evaluation of DNN Processors

## Slide 11: What are Deep Neural Networks?
Input:
Image
@eems_mit)
11
Output:
“Volvo XC90”
Modified Image Source: [Lee, CACM 2011]
Low Level Features
High Level Features

## Slide 12: Weighted Sums
Key operation is
multiply and accumulate (MAC)
Accounts for > 90% of computation
Yj
 activation
3
 i1

Xi 

Output Layer
Input Layer
Hidden Layer
X
1
X2
X3
Y
1
Y2
Y3
Y4
W
11
W34
Nonlinear 
Activation Wij
Function
Sigmoid
1
-1
-1
0
0
1
Rectified Linear Unit (ReLU) 1
@eems_mit)
12
-1
0
-1 0 1
y=max(0,x)
y=1/(1+e-x)
Image source: Caffe tutorial

## Slide 13: Popular Types of Layers in DNNs
Fully Connected Layer
  Feed forward, fully connected
  Multilayer Perceptron (MLP)
Convolutional Layer
  Feed forward, sparsely-connected w/ weight sharing
  Convolutional Neural Network (CNN)
  Typically used for images
Recurrent Layer
  Feedback
  Recurrent Neural Network (RNN)
Typically used for sequential data (e.g., speech, language)
Attention Layer/Mechanism
  Attention (matrix multiply) + feed forward, fully connected
  Transformer [Vaswani, NeurIPS 2017]
Feedback
Feed Forward
Input Layer
Output Layer
Hidden Layer
Input Layer
Output Layer
Hidden Layer
Sparsely Connected
Fully Connected
NeurIPS 2019
Vivienne Sze (
@eems_mit)
13

## Slide 14: High-Dimensional Convolution in CNN
S
a plane of input activations
a.k.a. input feature map (fmap)
filter (weights)
H
R
W
@eems_mit)

## Slide 15: High-Dimensional Convolution in CNN
S
Element-wise Multiplication
input fmap
filter (weights)
H
R
W
@eems_mit)

## Slide 16: High-Dimensional Convolution in CNN
R
filter (weights)
S
E
F
Partial Sum (psum)
Accumulation
input fmap
Element-wise Multiplication
H
W
@eems_mit)
output fmap
an output
activation

## Slide 17: High-Dimensional Convolution in CNN
H
R
filter (weights)
S
E
Sliding Window Processing
input fmap
activation
output fmap
an output
W
F
@eems_mit)

## Slide 18: High-Dimensional Convolution in CNN
AlexNet: 3 – 192 Channels (C)
H
R
S
…
…
…
C
input fmap
output fmap
…
…
…
…
C
…
filter
…
Many Input Channels (C)
E
W
F
@eems_mit)

## Slide 19: High-Dimensional Convolution in CNN
…
E
output fmap
…
…
many filters (M)
Many
Output Channels (M)
M
…
R
S
1
R
S
…
…
…
C
…
M
H
input fmap
…
…
…
…
C
…
C
…
…
…
W
F
@eems_mit)
AlexNet: 96 – 384 Filters (M)

## Slide 20: High-Dimensional Convolution in CNN
( @eems_mit) NeurIPS 2019
Vivienne Sze
…
M
…
Many
Input fmaps (N)
Many Output fmaps (N)
…
R
S
R
S
…
…
…
C
…
C
…
…
…
filters
…
E
F
…
…
H
…
…
C
…
H
W
…
…
…
…
C
…
…
E
…
…
1
1
N
N
W
F
Image
batch size:
1 – 256 (N)
20

## Slide 21: Define Shape for Each Layer
H – Height of input fmap (activations) W – Width of input fmap (activations) C – Number of 2-D input fmaps /filters (channels)
R – Height of 2-D filter (weights)
S – Width of 2-D filter (weights)
M – Number of 2-D output fmaps (channels)
E – Height of output fmap (activations)
F – Width of output fmap (activations)
N – Number of input fmaps/output fmaps (batch size)
Shape varies across layers
Filters
S
…
…
…
C
R M
H
W
…
…
C
…
E
F
…
…
…
M
…
…
…
M
…
R
S
…
…
…
C
H
W
…
…
C
1
N
1
1
…
……
Input fmaps
Output fmaps
…
E
F
@eems_mit)
N

## Slide 22: Layers with Varying Shapes
@eems_mit)
Block | Filter Size (RxS) | # Filters (M) | # Channels (C)
1 | 3x3 | 16 | 3
… |  |  | 
3 | 1x1 | 64 | 16
3 | 3x3 | 64 | 1
3 | 1x1 | 24 | 64
… |  |  | 
6 | 1x1 | 120 | 40
6 | 5x5 | 120 | 1
6 | 1x1 | 40 | 120
… |  |  | 
MobileNetV3-Large Convolutional Layer Configurations
[Howard, ICCV 2019]

## Slide 23: Popular DNN Models
Metrics | LeNet-5 | AlexNet | VGG-16 | GoogLeNet (v1) | ResNet-50 | EfficientNet-B4
Top-5 error (ImageNet) | n/a | 16.4 | 7.4 | 6.7 | 5.3 | 3.7*
Input Size | 28x28 | 227x227 | 224x224 | 224x224 | 224x224 | 380x380
# of CONV Layers | 2 | 5 | 16 | 21 (depth) | 49 | 96
# of Weights | 2.6k | 2.3M | 14.7M | 6.0M | 23.5M | 14M
# of MACs | 283k | 666M | 15.3G | 1.43G | 3.86G | 4.4G
# of FC layers | 2 | 3 | 3 | 1 | 1 | 65**
# of Weights | 58k | 58.6M | 124M | 1M | 2M | 4.9M
# of MACs | 58k | 58.6M | 124M | 1M | 2M | 4.9M
Total Weights | 60k | 61M | 138M | 7M | 25.5M | 19M
Total MACs | 341k | 724M | 15.5G | 1.43G | 3.9G | 4.4G
Reference | Lecun, PIEEE 1998 | Krizhevsky, NeurIPS 2012 | Simonyan, ICLR 2015 | Szegedy, CVPR 2015 | He, CVPR 2016 | Tan, ICML 2019
NeurIPS 2019
Vivienne Sze (
@eems_mit)
DNN models getting larger and deeper
* Does not include multi-crop and ensemble
** Increase in FC layers due to squeeze-and-excitation layers (much smaller than FC layers for classification)
23

## Slide 24: Key Metrics and Design Objectives
@eems_mit)

## Slide 25: Key Metrics: Much more than OPS/W!
Accuracy
  Quality of result
Throughput
  Analytics on high volume data
  Real-time performance (e.g., video at 30 fps)
Latency
  For interactive applications (e.g., autonomous navigation)
Energy and Power
  Embedded devices have limited battery capacity
  Data centers have a power ceiling due to cooling cost
Hardware Cost
  $$$
Flexibility
  Range of DNN models and tasks
Scalability
  Scaling of performance with amount of resources
ImageNet
Computer Vision
Speech Recognition
[Sze, CICC 2017]
MNIST CIFAR-10
Data Center
Embedded Device
@eems_mit)

## Slide 26: Key Design Objectives of DNN Processor
@eems_mit)
Increase Throughput and Reduce Latency
  Reduce time per MAC
    Reduce critical path  increase clock frequency
    Reduce instruction overhead
  Avoid unnecessary MACs (save cycles)
  Increase number of processing elements (PE)  more MACs in parallel
    Increase area density of PE or area cost of system
  Increase PE utilization*  keep PEs busy
    Distribute workload to as many PEs as possible
    Balance the workload across PEs
    Sufficient memory bandwidth to deliver workload to PEs (reduce idle cycles)
Low latency has an additional constraint of small batch size
*(100% = peak performance)

## Slide 27: Eyexam: Performance Evaluation Framework
Step 1: max workload parallelism (Depends on DNN Model)
Step 2: max dataflow parallelism
Number of PEs (Theoretical Peak Performance)
peak performance
MAC/cycle
@eems_mit)
MAC/data
[Chen, arXiv 2019: https://arxiv.org/abs/1807.07928 ]
A systematic way of understanding the performance limits for DNN hardware as a function of specific characteristics of the DNN model and hardware design

## Slide 28: Eyexam: Performance Evaluation Framework
Number of PEs (Theoretical Peak Performance)
peak performance
MAC/cycle
Slope = BW to PEs
Based on Roofline Model
MAC/data
Bandwidth (BW) Bounded
@eems_mit)
Compute Bounded
[Williams, CACM 2009]

## Slide 29: Eyexam: Performance Evaluation Framework
Step 1: max workload parallelism
peak performance
Step 2: max dataflow parallelism
Number of PEs (Theoretical Peak Performance) Step 3: # of active PEs under a finite PE array size
Step 4: # of active PEs under fixed PE array dimension Step 5: # of active PEs under fixed storage capacity
Slope = BW to only active PE
MAC/cycle
MAC/data
PE
C
M
https://arxiv.org/abs/1807.07928
Vivienne Sze ( @eems_mit)
NeurIPS 2019
29

## Slide 30: Eyexam: Performance Evaluation Framework
Step 1: max workload parallelism
peak performance
workload operational intensity
Step 2: max dataflow parallelism
Number of PEs (Theoretical Peak Performance) Step 3: # of active PEs under a finite PE array size
Step 4: # of active PEs under fixed PE array dimension Step 5: # of active PEs under fixed storage capacity
Step 6: lower act. PE util. due to insufficient average BW
Step 7: lower act. PE util. due to insufficient instantaneous BW
MAC/data
@eems_mit)
MAC/cycle
https://arxiv.org/abs/1807.07928

## Slide 31: Key Design Objectives of DNN Processor
Reduce Energy and Power Consumption
  Reduce data movement as it dominates energy consumption
    Exploit data reuse
  Reduce energy per MAC
    Reduce switching activity and/or capacitance
    Reduce instruction overhead
  Avoid unnecessary MACs
 Power consumption is limited by heat dissipation, which limits the maximum # of MACs in parallel (i.e., throughput)
Operation: | Energy (pJ)
8b Add | 0.03
16b Add | 0.05
32b Add | 0.1
16b FP Add | 0.4
32b FP Add | 0.9
8b Multiply | 0.2
32b Multiply | 3.1
16b FP Multiply | 1.1
32b FP Multiply | 3.7
32b SRAM Read (8KB) | 5
32b DRAM Read | 640
Relative Energy Cost
1 10 102 103 104
[Horowitz, ISSCC 2014]
@eems_mit)

## Slide 32: Key Design Objectives of DNN Processor
@eems_mit)
Flexibility
  Reduce overhead of supporting flexibility
  Maintain efficiency across wide range of DNN models
    Different layer shapes impact the amount of
      Required storage and compute
      Available data reuse that can be exploited
    Different precision across layers & data types (weight, activation, partial sum)
    Different degrees of sparsity (number of zeros in weights or activations)
    Types of DNN layers and computation beyond MACs (e.g., activation functions)
Scalability
  Increase how performance (i.e., throughput, latency, energy, power) scales with increase in amount of resources (e.g., number of PEs, amount of memory, etc.)

## Slide 33: Specifications to Evaluate Metrics
Accuracy
  Difficulty of dataset and/or task should be considered
  Difficult tasks typically require more complex DNN models
Throughput
  Number of PEs with utilization (not just peak performance)
  Runtime for running specific DNN models
Latency
  Batch size used in evaluation
Energy and Power
  Power consumption for running specific DNN models
  Off-chip memory access (e.g., DRAM)
Hardware Cost
  On-chip storage, # of PEs, chip area + process technology
Flexibility
  Report performance across a wide range of DNN models
  Define range of DNN models that are efficiently supported
DRAM
Chip
[Sze, CICC 2017]
Computer Vision
Speech Recognition
Off-chip memory access
ImageNet
MNIST CIFAR-10
@eems_mit)

## Slide 34: Comprehensive Coverage for Evaluation
@eems_mit)
All metrics should be reported for fair evaluation of design tradeoffs
Examples of what can happen if a certain metric is omitted:
  Without the accuracy given for a specific dataset and task, one could run a simple DNN and claim low power, high throughput, and low cost – however, the processor might not be usable for a meaningful task
  Without reporting the off-chip memory access, one could build a processor with only MACs and claim low cost, high throughput, high accuracy, and low chip power – however, when evaluating system power, the off-chip memory access would be substantial
Are results measured or simulated? On what test data?

## Slide 35: Example Evaluation Process
@eems_mit)
The evaluation process for whether a DNN processor is a viable solution for a given application might go as follows:
Accuracy determines if it can perform the given task
Latency and throughput determine if it can run fast enough and in real-time
Energy and power consumption will primarily dictate the form factor of the device where the processing can operate
Cost, which is primarily dictated by the chip area, determines how much one would pay for this solution
Flexibility determines the range of tasks it can support

## Slide 36: CPU & GPU Platforms
@eems_mit)

## Slide 37: CPUs and GPUs Targeting DNNs
Intel Xeon (Cascade Lake)
Nvidia Tesla (Volta)
Use matrix multiplication libraries on CPUs and GPUs
AMD Radeon (Instinct)
@eems_mit)

## Slide 38: Map DNN to a Matrix Multiplication
Fully connected layer can be directly represented as matrix multiplication
M
Filters
CHW
CHW
Input fmaps
N
×
Output fmaps
N
M
=
Note: Matrix multiplication also heavily used by recurrent and attention layers
In fully connected layer, filter size (R, S) same as input size (H, W)
H
W
…
…
…
C
…
1
…
M
…
filters input fmaps
output fmaps
…
…
…
…
H
…
…
C
…
…
1
…
…
N
N
1
1
W
1
H
…
…
C
…
M
W
H
W
…
…
…
C
…
1
1
@eems_mit)
M

## Slide 39: Map DNN to a Matrix Multiplication
Convolutional layer can be converted to Toeplitz Matrix
Convolution
1 | 2 | 3
4 | 5 | 6
7 | 8 | 9
1 | 2
3 | 4
Filter
Input Fmap
Output Fmap
*
=
1 | 2
3 | 4
1 | 2 | 3 | 4
1 | 2 | 4 | 5
2 | 3 | 5 | 6
4 | 5 | 7 | 8
5 | 6 | 8 | 9
1 | 2 | 3 | 4
×
=
Filter
Input Fmap
Output Fmap
Matrix Multiply (by Toeplitz Matrix)
Data is repeated
@eems_mit)

## Slide 40: CPU, GPU Libraries for Matrix Multiplication
@eems_mit)
Implementation: Matrix Multiplication (GEMM)
  CPU: OpenBLAS, Intel MKL, etc
  GPU: cuBLAS, cuDNN, etc
Library will note shape of the matrix multiply and select implementation optimized for that shape
Optimization usually involves proper tiling to memory hierarchy

## Slide 41: Tiling Matrix Multiplication
CHW
W
N
N
Matrix multiplication tiled to fit in cache (i.e., on-chip memory) and computation ordered to maximize reuse of data in cache
M
Filters
CHW
F0,0 | F0,1
F1,0 | F1,1
CCHHW
 | I0,0 | I0,1
 | I1,0 | I1,1
Input fmaps
N
×
Output fmaps
N
F0,0I0,0 + F0,1I1,0 | F0,0I0,1 + F0,1I1,1
F1,0I0,0 | F1,0I0,1
+ | +
F1,1I1,0 | F1,1I1,1
M
=
Step 1
M
Filters
CHW
F0,0 | F0,1
F1,0 | F1,1
I0,0 | I0,1
I1,0 | I1,1
CHW
Input fmaps
N
×
Output fmaps
N
F0,0I0,0 + F0,1I1,0 | F0,0I0,1 + F0,1I1,1
F1,0I0,0 | F1,0I0,1
+ | +
F1,1I1,0 | F1,1I1,1
M
@eems_mit)
=
Step 2

## Slide 42: Analogy: Gauss’s Multiplication Algorithm
4 multiplications + 3 additions
@eems_mit)
3 multiplications + 5 additions
Reduce number of multiplications to
increase throughput

## Slide 43: Reduce Operations in Matrix Multiplication
@eems_mit)
Fast Fourier Transform [Mathieu, ICLR 2014]
  Pro: Direct convolution O(No2Nf ) to O(No log2No)
2 2
  Con: Increase storage requirements
Strassen [Cong, ICANN 2014]
  Pro: O(N3) to (N2.807)
  Con: Numerical stability
Winograd [Lavin, CVPR 2016]
  Pro: 2.25x speed up for 3x3 filter
  Con: Specialized processing depending on filter size
Compiler selects transform based on filter size

## Slide 44: Reduce Instruction Overhead
Perform more MACs per instruction
  CPU: SIMD / Vector Instructions
    e.g., Specialized Vector Neural Network Instructions (VNNI) fuse separate multiply and add instructions into single MAC instruction and avoid storing intermediate values in memory
  GPU: SIMT / Tensor Instructions
    e.g., New opcode Matrix Multiply Accumulate (HMMA) performs 64 MACs with Tensor Core
Perform more MACs per cycle without increasing memory bandwidth by adding support for reduced precision
  e.g., If access 512 bits per cycle, can perform 64 8-bit MACs vs. 16 32-bit MACs
Tensor Core
Image Source: Nvidia
@eems_mit)

## Slide 45: Design Considerations for CPU and GPU
@eems_mit)
Software (compiler)
  Reduce unnecessary MACs: Apply transforms
  Increase PE utilization: Schedule loop order and tile data to increase data reuse in memory hierarchy
Hardware
  Reduce time per MAC
    Increase speed of PEs
    Increase MACs per instruction using large aggregate instructions (e.g., SIMD, tensor core)
 requires additional hardware
  Increase number of parallel MACs
    Increase number of PEs on chip  area cost
    Support reduced precision in PEs
  Increase PE utilization
    Increase on-chip storage  area cost
    External memory BW  system cost

## Slide 46: Specialized / Domain- Specific Hardware
@eems_mit)

## Slide 47: Properties We Can Leverage
Worst Case: all memory R/W are DRAM accesses
Example: AlexNet has 724M MACs  2896M DRAM accesses required
ALU
Memory Write
Operations exhibit high parallelism
 high throughput possible
Memory Access is the Bottleneck
Memory Read MAC*
* multiply-and-accumulate
filter weight fmap act partial sum
updated partial sum
200x 1x
DRAM
DRAM
@eems_mit)

## Slide 48: Properties We Can Leverage
Operations exhibit high parallelism
 high throughput possible
Input data reuse opportunities (e.g., up to 500x for AlexNet)
 exploit low-cost memory
Input Fmaps
Vivienne Sze ( @eems_mit)
NeurIPS 2019
Filter
Input Fmap Filters
Convolutional Reuse (Activations, Weights) CONV layers only
(sliding window)
2
1
Input Fmap
Fmap Reuse
(Activations) CONV and FC layers
Filter
2
1
Filter Reuse
(Weights)
CONV and FC layers (batch size > 1)
48

## Slide 49: Highly-Parallel Compute Paradigms
Temporal Architecture (SIMD/SIMT)
Spatial Architecture (Dataflow Processing)
Register File
Memory Hierarchy
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
Control
Memory Hierarchy
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
NeurIPS 2019
Vivienne Sze (
@eems_mit)
49

## Slide 50: Advantages of Spatial Architecture
Temporal Architecture
(SIMD/SIMT)
Memory Hierarchy
Register File
ALU ALU ALU ALU
ALU ALU ALU ALU
ALU ALU ALU ALU ALU ALU ALU ALU
Control
Spatial Architecture (Dataflow Processing)
Memory Hierarchy
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
Efficient Data Reuse
Distributed local storage (RF)
Inter-PE Communication
Sharing among regions of PEs
Processing Element (PE)
Control
Reg File
0.5 – 1.0 kB
@eems_mit)

## Slide 51: How to Map the Dataflow?
Spatial Architecture (Dataflow Processing)
Memory Hierarchy
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
CNN Convolution
?
activations weights
partial sums
Goal: Increase reuse of input data (weights and activations) and local partial sums accumulation
@eems_mit)

## Slide 52
Efficient Dataflows
@eems_mit)
Y.-H. Chen, J. Emer, V. Sze,
“Eyeriss: A Spatial Architecture for Energy-Efficient Dataflow for Convolutional Neural Networks,”
International Symposium on Computer Architecture (ISCA), June 2016.

## Slide 53: Data Movement is Expensive
Maximize data reuse at low cost levels of memory hierarchy
DRAM
Global
Buffer
PE
PE
PE
ALU
fetch data to run a MAC here
ALU
Buffer
ALU
RF
ALU
Normalized Energy Cost*
200×
6×
PE
ALU
2×
1×
1× (Reference)
DRAM
ALU
0.5 – 1.0 kB
@eems_mit)
100 – 500 kB
NoC: 200 – 1000 PEs
* measured from a commercial 65nm process
Specialized hardware with small (< 1kB) low cost memory near compute
Farther and larger memories consume more power

## Slide 54: Weight Stationary (WS)
Global Buffer
W0
W1
W2
W3
W4
W5
W6
W7
Psum
Activation
PE
Weight
Minimize weight read energy consumption
− maximize convolutional and filter reuse of weights
Broadcast activations and accumulate partial sums spatially
across the PE array
[Chen, ISCA 2016]
• Examples: TPU [Jouppi, ISCA 2017], NVDLA
@eems_mit)

## Slide 55: Output Stationary (OS)
Broadcast/Multicast filter weights and reuse activations spatially
across the PE array
Global Buffer
P0
P1
P2
P3
P4
P5
P6
P7
Activation Weight
PE
Psum
Minimize partial sum R/W energy consumption
− maximize local accumulation
• Examples: [Moons, VLSI 2016], [Thinker, VLSI 2017]
@eems_mit)
[Chen, ISCA 2016]

## Slide 56: Input Stationary (IS)
Minimize activation read energy consumption
− maximize convolutional and fmap reuse of activations
Unicast weights and accumulate partial sums spatially
across the PE array
Global Buffer
I0 I1 I2 I3 I4 I5 I6 I7
Act
• Example: [SCNN, ISCA 2017]
@eems_mit)
Weight Psum
PE
[Chen, ISCA 2016]

## Slide 57: Row Stationary Dataflow
Maximize row convolutional reuse in RF
− Keep a filter row and fmap sliding window in RF
Maximize row psum accumulation in RF
PE
Reg File
c b a
e d c
c
b
a
1D convolution within PE
[Chen, ISCA 2016]
57
@eems_mit)

## Slide 58: Row Stationary Dataflow
Optimize for
overall energy efficiency instead for only a certain data type
PE 1
Row 1
Row 1
PE 2
Row 2
Row 2
PE 3
Row 3
Row 3
Row 1
=
PE 4
Row 1
Row 2
PE 5
Row 2
Row 3
PE 6
Row 3
Row 4
Row 2
=
PE 7
Row 1
Row 3
PE 8
Row 2
Row 4
PE 9
Row 3
Row 5
Row 3
* * *
=
[Chen, ISCA 2016]
58
@eems_mit)
*
*
*
*
*
*
*
*
*

## Slide 59: Eyeriss: Deep Neural Network Accelerator
On-chip Buffer
4mm
Spatial PE Array
4mm
[Chen, ISSCC 2016]
Exploits data reuse for 100x reduction in memory accesses from global buffer and 1400x reduction in memory accesses from off-chip DRAM
Overall >10x energy reduction compared to a mobile GPU (Nvidia TK1)
Vivienne Sze ( @eems_mit) NeurIPS 2019
59
Results for AlexNet

## Slide 60: Features: Energy vs. Accuracy
0.1
1
10
100
1000
0
20
40 60
Accuracy (Average Precision)
80
Energy/Pixel (nJ)
AlexNet
2
HOG1
Exponential
10000 VGG162
Measured in on VOC 2007 Dataset
1. DPM v5 [Girshick, 2012]
2. Fast R-CNN [Girshick, CVPR 2015]
Linear
Video Compression
[Suleiman, ISCAS 2017]
Vivienne Sze ( @eems_mit)
Measured in 65nm*
On-chip Buffer
Spatial
PE Array
4mm
4mm
4mm
4mm
1 [Suleiman, VLSI 2016] 2 [Chen, ISSCC 2016]
* Only feature extraction. Does not include data, classification energy, augmentation and ensemble, etc.
NeurIPS 2019
60

## Slide 61: Break for Q&A
@eems_mit)

## Slide 62: Algorithm (DNN Model) & Hardware Co-Design
@eems_mit)

## Slide 63: Algorithm & Hardware Co-Design
@eems_mit)
Co-design algorithm + hardware  better than what each could achieve alone
Co-design approaches can be loosely grouped into two categories:
  Reduce size of operands for storage/compute (Reduced Precision)
  Reduce number of operations for storage/compute (Sparsity and Efficient Network Architecture)
Hardware support required to increase savings in latency and energy
  Ensure that overhead of hardware support does not exceed benefits
Unlike previously discussed approaches, these approaches can affect accuracy!
  Evaluate tradeoff between accuracy and other metrics

## Slide 64: Reduced Precision
@eems_mit)

## Slide 65: Why Reduce Precision (i.e., Reduce Bit Width)?
Reduce data movement and storage cost for inputs and outputs of MAC
  Smaller memory  lower energy
Reduce cost of MAC
  Cost of multiply increases with bit width (n)  energy and area by O(n2); delay by O(n)
HA
x3
FA
x2
FA
x1
FA
x2
FA
x1
HA
x0
FA
x1
HA
x0
HA
x0
FA
x3
FA
x2
FA
x3
x3
x2
x1
x0
z0
z1
z2
z3
z7 z6 z5 z4
y3
y2
y1
y0
Note: Bit width for multiplication and accumulation in a MAC are different
@eems_mit)

## Slide 66: Impact of Reduced Precision on Energy & Area
[Horowitz, ISSCC 2014]
Operation: | Energy (pJ) |  |  | 
8b Add | 0.03 |  |  | 
16b Add | 0.05 |  |  | 
32b Add | 0.1 |  |  | 
16b FP Add | 0.4 |  |  | 
32b FP Add | 0.9 |  |  | 
8b Mult | 0.2 |  |  | 
32b Mult | 3.1 |  |  | 
16b FP Mult | 1.1 |  |  | 
32b FP Mult | 3.7 |  |  | 
32b SRAM Read (8KB) | 5 |  |  | 
32b DRAM Read | 640 |  |  | 
Area (m2)
36
67
137
1360
4184
282
3495
1640
7700
N/A
N/A
1 10 102 103 104
Relative Energy Cost Relative Area Cost
1 10 102 103
@eems_mit)

## Slide 67: What Determines Bit Width?
Number of unique values
  e.g., M-bits to represent 2M values
Dynamic range of values
  e.g., E-bits to scale values by 2(E-127)
Signed or unsigned values
  e.g., signed requires one extra bit (S)
Total bits = S+E+M
Floating point (FP) allows range to change for each value (E-bits)
Fixed point (Int) has fixed range
 Default CPU/GPU is 32-bit float (FP32)
FP32
FP16
Int32
Int16
Int8
S | E | M
1 8
23
S | E | M
1
5
10
M
31
S
S
M
1
1
15
S
@eems_mit)
M
1
7
Range
10-38 – 1038
6x10-5 - 6x104
0 – 2x109
0 – 6x104
0 – 127
Image Source: B. Dally
Common Numerical Representations

## Slide 68: What Determines Bit Width?
@eems_mit)
For accuracy, require sufficient precision to represent different data types
  For inference: weights, activations, and partial sums
  For training: weights, activations, partial sums, gradients,
and weight update
  Required precision can vary across data types
 Referred to as mixed precision

## Slide 69: What Determines Bit Width?
Reduce number of unique values (M-bits, a.k.a. mantissa)
  Default: Uniform quantization (values are equally spaced out)
  Non-uniform quantization (spacing can be computed, e.g., logarithmic, or with look-up-table)
  Fewer unique values can make transforms and compression more effective
Image Source:[Lee, ICASSP 2017]
@eems_mit)

## Slide 70: What Determines Bit Width?
@eems_mit)
Reduce number of unique values (M-bits, a.k.a. mantissa)
  Default: Uniform quantization (values are equally spaced out)
  Non-uniform quantization (spacing can be computed, e.g., logarithmic, or with look-up-table)
  Fewer unique values can make transforms and compression more effective
Reduce dynamic range (E-bits, a.k.a., exponent)
  If possible, fix range (i.e., used fixed point, E=0)
  Share range across group of values (e.g., weights for a layer or channel)
Tradeoff between number of bits allocated to M-bits and E-bits
S | E | E | E | E | E | M | M | M | M | M | M | M | M | M | M
fp16 (S=1, E=5, M=10)
bfloat16 (S=1, E=8, M=7)
S | E | E | E | E | E | E | E | E | M | M | M | M | M | M | M
range: ~5.9e-8 to ~6.5e4
range: ~1e-38 to ~3e38

## Slide 71: Commercial Products Support Reduced Precision
Nvidia’s Pascal (2016)
Google’s TPU (2016) TPU v2 & v3 (2019)
8-bit fixed for Inference & 16-bit float for Training
Intel’s NNP-L (2019)
@eems_mit)

## Slide 72: Reduced Precision in Research
Reduce number of bits
  Binary Nets [Courbariaux, NeurIPS 2015]
Reduce number of unique weights and/or activations
  Ternary Weight Nets [Li, NeurIPS Workshop 2016]
  XNOR-Net [Rategari, ECCV 2016]
Non-Linear Quantization
LogNet [Lee, ICASSP 2017]
Training
  8-bit with stochastic rounding
[Wang, NeurIPS 2018]
Binary Filters
Log Domain Quantization
@eems_mit)

## Slide 73: Precision Scalable MACs for Varying Precision
Conventional data-gated MAC Gate unused logic (e.g., full adders) to reduce energy consumption
[Camus, JETCAS 2019]
Full precision 8bx8b
4bx4b
2bx8b
Many approaches add logic to increase utilization for higher throughput/area; however, overhead can reduce benefits
4bx4b
1.3x
1.6x
Evaluation of 19 precision scalable MAC designs
5% of values 8bx8b
95% of values at 2bx2b and 4bx4b
Conventional
data-gated
@eems_mit)

## Slide 74: Design Considerations for Reduced Precision
@eems_mit)
Impact on accuracy
  Must consider difficulty of dataset, task, and DNN model
    e.g., Easy to reduce precision for an easy task (e.g., digit classification); does method work for a more difficult task?
Does hardware cost exceed benefits?
  Need extra hardware to support variable precision
    e.g., Additional shift-and-add logic and registers for variable precision
  Granularity impacts hardware overhead as well as accuracy
    e.g., More overhead to support (1b, 2b, 3b … 16b) than (2b, 4b, 8b, 16b)
Evaluation
  Use 8-bit for inference and 16-bit float for training for baseline
  32-bit float is a weak baseline

## Slide 75: Sparsity
@eems_mit)

## Slide 76: Why Increase Sparsity?
@eems_mit)
Reduce number of MACs
  Anything multiplied by zero is zero  avoid performing unnecessary MACs
  Reduce energy consumption and latency
Reduce data movement
  If one of the inputs to MAC is zero, can avoid reading the other input
  Compress data by only sending non-zero values
CPU/GPU libraries typically only support really high sparsity (> 99%) due to the overhead
  Sparsity for DNNs typically much lower  need specialized hardware

## Slide 77: Sparsity in Activation Data
9 | -1 | -3
1 | -5 | 5
-2 | 6 | -1
Many zeros in output fmaps after ReLU
ReLU
9 | 0 | 0
1 | 0 | 5
0 | 6 | 0
1
0.8
0.6
0.4
0.2
0
1
2
3
CONV Layer
4
5
# of activations
# of non-zero activations
@eems_mit)
(Normalized)
[Chen, ISSCC 2016]

## Slide 78: Data Gating / Zero Skipping
Eyeriss [Chen, ISSCC 2016]
Filter Scratch Pad
(225x16b SRAM)
Partial Sum
Scratch Pad
(24x16b REG)
Filt
Img
Input Psum
2-stage pipelined multiplier
Output Psum
0
Accumulate Input Psum
1
0
== 0
Zero
Buffer
Enable
Image Scratch Pad (12x16b REG)
0
1
Skip MAC and mem reads
when image data is zero.
Reduce PE power by 45%
Reset
Cnvlutin [Albericio, ISCA 2016]
Gate operations
(reduce power consumption)
Skip operations
(increase throughput)
@eems_mit)

## Slide 79: Apply Compression to Reduce Data Movement
Simple RLC within 5% - 10% of theoretical entropy limit
[Chen, ISSCC 2016]
1 2 3 4 5
AlexNet Conv Layer
DRAM
Access (MB)
6
4
2
0
1.2×
1.4×
1.7×
1.8×
1.9×
Uncompressed Fmaps + Weights
RLE Compressed Fmaps + Weights
Example: Eyeriss compresses activations to reduce DRAM BW
Link Clock Core Clock
14×12 PE Array
Filter Filt
…
Input Image Buffer Img …
SRAM
Psum
…
Output Image 108KB
Psum … …
ReLU
…
Output (64b):
Run-Length Compression (RLC)
Example:
Input: 0, 0, 12, 0, 0, 0, 0, 53, 0, 0, 22, …
RunLevelRunLevel RunLevelTerm
2 12 4 53 2 22 0
5b 16b 5b 16b 5b 16b 1b
Off-Chip DRAM
64 bits
Decomp
Comp
DCNN Accelerator
DNN Accelerator
@eems_mit)

## Slide 80: Pruning – Make Weights Sparse
Optimal Brain Damage
[Lecun, NeurIPS 1990]
pruning neurons
pruning synapses
Prune DNN based on
magnitude of weights
before pruning after pruning
Example: AlexNet
Weight Reduction: CONV layers 2.7x,
FC layers 9.9x
Overall Reduction: Weights 9x, MACs 3x
[Han, NeurIPS 2015]
retraining
@eems_mit)

## Slide 81: Unstructured or Structured Sparsity
Increase coarseness
@eems_mit)
Image Source: [Mao, CVPR Workshop 2017]
Benefits:
Increase coarseness  more structure in sparsity (easier for hardware) Less signaling overhead for location of zeros  better compression

## Slide 82: Design Considerations for Sparsity
@eems_mit)
Impact on accuracy
  Must consider difficulty of dataset, task, and DNN model
    e.g., AlexNet and VGG known to be over parameterized and thus easy to prune weights; does method work on efficient DNN models?
Does hardware cost exceed benefits?
  Need extra hardware to identify sparsity
    e.g., Additional logic to identify non-zeros and store non-zero locations
  Accounting for sparsity in both weights and activations is challenging
    Need to compute intersection of two data streams rather than find next non-zero in one
  Granularity impacts hardware overhead as well as accuracy
    e.g., Fine-grained or coarse-grained (structured) sparsity
  Compressed data will be variable length
    Reduced flexibility in access order  random access will have significant overhead

## Slide 83: Efficient Network Architectures
@eems_mit)

## Slide 84: Efficient DNN Models
 | Year | Accuracy* | # Layers | # Weights | # MACs
AlexNet | 2012 | 80.4% | 8 | 61M | 724M
MobileNet | 2017 | 89.5% | 28 | 4M | 569M
[1]
* ImageNet Classification Top-5
Filter Decomposition
R
S
C
…
…
…
R
S
…
…
C
1
* 1
Bottleneck Layer
Reduce number of channels before large filter convolution
Decompose large filters into smaller filters
Design efficient DNN Models
  Tends to increase variation of layer shapes (e.g., R, S, C) that need to be supported
  Can be handcrafted or learned using Network/Neural Architecture Search (NAS)
Filter Decomposition 1x1 convolutions
@eems_mit)

## Slide 85: Manual Network Design
Reduce Spatial Size (R, S)
  stacked filters
Reduce Channels (C)
  1x1 convolution, group of filters
Reduce Filters (M)
  feature map reuse across layers
Layer Pooling
  global pooling before FC layer
Filters
S
…
…
…
C
R M
H
W
…
…
C
…
E
F
…
…
…
M
…
…
…
M
…
R
S
…
…
…
C
H
W
…
…
C
1
N
1
1
…
……
Input fmaps
Output fmaps
…
E
F
@eems_mit)
N

## Slide 86: Reduce Spatial Size (R, S): Stacked Filter
decompose
5x5 filter
5x1 filter
1x5 filter
Apply sequentially
GoogleNet/ Inception v3
separable filters
5x5 filter
Two 3x3 filters
decompose
@eems_mit)
Apply sequentially
VGG
Replace a large filter with a series of smaller filters

## Slide 87: Reduce Channels (C): 1x1 Convolution
Use 1x1 filter to summarize cross-channel information
Modified image from source:
Stanford cs231n
[Lin, ICLR 2014]
56
1
@eems_mit)
56
filter1 (1x1x64)

## Slide 88: Reduce Channels (C): 1x1 Convolution
Use 1x1 filter to summarize cross-channel information
filter2 (1x1x64)
2
Modified image from source:
Stanford cs231n
[Lin, ICLR 2014]
88
@eems_mit)
56
56

## Slide 89: Reduce Channels (C): 1x1 Convolution
Use 1x1 filter to summarize cross-channel information
56
32
Modified image from source:
Stanford cs231n
[Lin, ICLR 2014]
89
@eems_mit)
56

## Slide 90: GoogLeNet:1x1 Convolution
1x1 convolutions to reduce number of weights and multiplications
Apply 1x1 convolution before ‘large’ convolution filters.
Reduce weights such that entire CNN can be trained on one GPU.
Number of multiplications reduced from 854M  358M
Inception Module
@eems_mit)
90
[Szegedy, CVPR 2015]

## Slide 91: Reduce Channels (C): Group of Filters
Split filters and channels of feature map into different groups
e.g., For two groups, each filter requires 2x fewer weights and multiplications
H
R
S
…
…
…
input fmap
output fmap1
…
…
…
…
C
…
C/2 filter1
E
W
F
input fmap
output fmap2
…
…
E
F
H
…
…
…
…
C
W
R
…
…
…
C/2 filter2
S
@eems_mit)

## Slide 92: Reduce Channels (C): Group of Filters
The extreme case is depthwise convolution – each group contains only one channel
H
R
S
output fmap1
…
…
…
…
input fmap
C
…
filter1
E
W
F
input fmap
output fmapC
…
…
E
F
H
…
…
…
…
C
W
R
filterC
S
@eems_mit)

## Slide 93: Reduce Channels (C): Group of Filters
Two ways of mixing information across groups
Pointwise (1x1) Convolution (Mix in one step)
MobileNet [Howard, arXiv 2017]
Shuffle Operation (Mix in multiple steps)
ShuffleNet [Zhang, CVPR 2018]
C
1
+ 1
S
R
1
R
S
C
fmap 0
@eems_mit)
layer 1
fmap 1
layer 2
fmap 2

## Slide 94: Reduce Filters (M): Feature Map Reuse
…
R
S
1
C
…
…
…
M Filters
…
R
S
K
C
…
…
…
…
C… …
R
M …
S
Output fmap with M channels
L 2
L 3
L 1
DenseNet reuses feature map from multiple layers
[Huang, CVPR 2017]
M
F
Reuse (M-K) channels in feature maps from previously processed layers
……
……
E
K
M-K
@eems_mit)

## Slide 95: Layer Pooling: Simplify FC Layers
First FC layer accounts for a significant portion of weights
38M of 61M for AlexNet
[Krizhevsky, NeurIPS 2012]
105M
# of MACs
L1
L2
L3
L4
L5
L6
L7
1000
scores
224x224
Input Image
Conv (11x11) | Non-Linearity | Norm (LRN) | Max Pool
Conv (5x5) | Non-Linearity | Norm (LRN) | Max Pooling
Conv (3x3) Non-Linearity
Conv (3x3) Non-Linearity
Conv (3x3) Non-Linearity Max Pooling
Fully Connect Non-Linearity
Fully Connect Non-Linearity
Fully Connect
34k
307k
224M
885k
150M
664k
112M
442k
75M
37.7M
# of weights
38M 16.8M 4.1M
38M 17M 4M
@eems_mit)

## Slide 96: Layer Pooling: Simplify FC Layers
[Lin, ICLR 2014]
Global Pooling reduces the size of the input to the first FC layer, which reduces its size
(e.g., HxWxCx1000  1x1xCx1000)
H
…
output fmap1
…
1
W
1
H
…
…
W
…
filter1 input fmap
C C
H
input fmap
output fmap1
…
C
1
W
@eems_mit)
96
1
Pool

## Slide 97: Network/Neural Architecture Search (NAS)
3x3? 5x5?
128 Filters?
Pool? CONV?
Rather than handcrafting the architecture, automatically search for it
@eems_mit)
97

## Slide 98: Network/Neural Architecture Search (NAS)
Three main components:
  Search Space (what is the set of all samples)
  Optimization Algorithm (where to sample)
  Performance Evaluation (how to evaluate samples)
Key Metrics: Achievable DNN accuracy and required search time
Search Space
Performance Evaluation
Evaluation Result
Optimization Algorithm
Next Location to Sample
Sampled Network
Final Network
@eems_mit)
98

## Slide 99: Evaluate NAS Search Time
𝑡i𝑚𝑒𝑛𝑎𝑠 = 𝑛𝑢𝑚𝑠𝑎𝑚𝑝𝑙𝑒𝑠 × 𝑡i𝑚𝑒𝑝𝑒𝑟_𝑠𝑎𝑚𝑝𝑙𝑒
𝑡i𝑚𝑒𝑛𝑎𝑠 𝖺
𝑛𝑢𝑚𝑛𝑎𝑠_𝑡𝑢𝑛i𝑛𝑔 × 𝑛𝑢𝑚𝑛𝑎𝑠_𝑠𝑡𝑒𝑝𝑠 × 𝑠i1𝑒𝑠𝑒𝑎𝑟𝑐3_𝑠𝑝𝑎𝑐𝑒
× (𝑡i𝑚𝑒𝑡𝑟𝑎i𝑛 + 𝑡i𝑚𝑒𝑒𝑣𝑎𝑙)
(1) Shrink the search space
(2) Improve the optimization algorithm
(3) Simplify the performance
evaluation
Goal: Improve the efficiency of NAS in the three main components
Search Space
Performance Evaluation
Optimization Algorithm
@eems_mit)
99

## Slide 100: (1) Shrink the Search Space
 Trade the breadth of architectures for search speed
 May limit the performance that can be achieved
 Use domain knowledge from manual network design to help guide the reduction of the search space
Architecture Universe
Search Space
Optimal
Optimal
Samples =
@eems_mit)
100

## Slide 101: (1) Shrink the Search Space
@eems_mit)
101
Identity
1x3 then 3x1 convolution
1x7 then 7x1 convolution
3x3 dilated convolution
1x1 convolution
3x3 convolution
 Search space = layer operations + connections between layers
Common layer operations
3x3 separable convolution
5x5 separable convolution
3x3 average pooling
3x3 max pooling
5x5 max pooling
7x7 max pooling
[Zoph, CVPR 2018]

## Slide 102: (1) Shrink the Search Space
Image Source: [Zoph, CVPR 2018]
 Search space = layer operations + connections between layers
Smaller Search Space
@eems_mit)
102

## Slide 103: (2) Improve Optimization Algorithm
Random Coordinate Descent Gradient Descent
Reinforcement Learning
@eems_mit)
103
Bayesian
Evolutionary

## Slide 104: (3) Simplify the Performance Evaluation
NAS needs only the rank of the performance values
Method 1: approximate accuracy
Proxy Task
Early Termination
Accuracy Prediction
E.g., Smaller resolution, simpler tasks
Accuracy
Iteration
Stop training earlier
Stop
Extrapolate accuracy
Accuracy
Iteration
Predict
@eems_mit)
104

## Slide 105: (3) Simplify the Performance Evaluation
NAS needs only the rank of the performance values
Method 2: approximate weights
Copy Weights
Estimate Weights
Reuse weights from other similar networks
Infer the weights from the previous feature maps
Copy
Generate
@eems_mit)
105
What weights?
Previous
New
Feature Map
Filter
Previous
New

## Slide 106: (3) Simplify the Performance Evaluation
NAS needs only the rank of the performance values
Method 3: approximate metrics (e.g., latency, energy)
Look-Up Table
Proxy Metric
Use an easy-to-compute metric to approximate target
Use table lookup
Latency
@eems_mit)
106
# MACs

## Slide 107: Design Considerations for NAS
@eems_mit)
107
The components may not be chosen individually
  Some optimization algorithms limit the search space
  Type of performance metric may limit the selection of the optimization algorithms
Commonly overlooked properties
  The complexity of implementation
  The ease of tuning hyperparameters of the optimization
  The probability of convergence to a good architecture

## Slide 108: Hardware In the Loop
@eems_mit)
108

## Slide 109: How to Evaluate Complexity of DNN Model?
Number of MACs and weights are not good proxies for latency and energy
# of operations (MACs) does not approximate latency well
Source: Google
(https://ai.googleblog.com/2018/04/introducing-cvpr-2018-on-device-visual.html)
Output Feature Map 43%
@eems_mit)
109
Input Feature Map 25%
Weights 22%
10%
# of weights alone is not a good metric for energy (All data types should be considered)
Computation
https://energyestimation.mit.edu/
[Yang, CVPR 2017]
Energy breakdown of GoogLeNet

## Slide 110: Energy-Aware Pruning
Directly target energy
and incorporate it into the
optimization of DNNs to provide greater energy savings
Sort layers based on energy and prune layers that consume the most energy first
Energy-aware pruning reduces AlexNet energy by 3.7x and outperforms the previous work that uses magnitude- based pruning by 1.7x
4
3.5
3
2.5
2
1.5
1
0.5
0
4.5 x109
Ori.
DC
EAP
Normalized Energy (AlexNet)
2.1x
3.7x
Magnitude Based Pruning
Energy Aware Pruning
@eems_mit)
110
Pruned models available at http://eyeriss.mit.edu/energy.html
[Yang, CVPR 2017]

## Slide 111: NetAdapt: Platform-Aware DNN Adaptation
Automatically adapt DNN to a mobile platform to reach a target latency or energy budget
Use empirical measurements to guide optimization (avoid modeling of tool chain or platform architecture)
Requires very few hyperparameters to tune
In collaboration with Google’s Mobile Vision Team
NetAdapt
Measure
…
Empirical Measurements
Metric | Proposal A | … | Proposal Z
Latency | 15.6 | … | 14.3
… | … |  | …
Energy | 41 | … | 46
Pretrained Network
Metric | Budget
Latency | 3.8
… | …
Energy | 10.5
Network Proposals A B C D
Budget
Adapted Network
Platform
Z
@eems_mit)
111
[Yang, ECCV 2018]
Code available at http://netadapt.mit.edu

## Slide 112: Improved Latency vs. Accuracy Tradeoff
 NetAdapt boosts the measured inference speed of MobileNet by up to 1.7x with higher accuracy
Reference:
MobileNet: Howard et al, “Mobilenets: Efficient convolutional neural networks for mobile vision applications,” arXiv 2017
MorphNet: Gordon et al., “Morphnet: Fast & simple resource-constrained structure learning of deep networks,” CVPR 2018
+0.3% accuracy 1.7x faster
+0.3% accuracy 1.6x faster
@eems_mit)
112
*Tested on the ImageNet dataset and a Google Pixel 1 CPU

## Slide 113: Design Considerations for Co-Design
@eems_mit)
113
Impact on accuracy
  Consider quality of baseline (initial) DNN model, difficulty of task and dataset
  Sweep curve of accuracy versus latency/energy to see the full tradeoff
Does hardware cost exceed benefits?
  Need extra hardware to support variable precision and shapes or to identify sparsity
  Granularity impacts hardware overhead as well as accuracy
Evaluation
  Avoid only evaluating impact based on number of weights or MACs as they may not be sufficient for evaluating energy consumption and latency

## Slide 114: Design Considerations for Co-Design
@eems_mit)
114
Time required to perform co-design
  e.g., Difficulty of tuning affected by
    Number of hyperparameters
    Uncertainty in relationship between hyperparameters and impact on performance
Other aspects that affect accuracy, latency or energy
  Type of data augmentation and preprocessing
  Optimization algorithm, hyperparameters, learning rate schedule, batch size
  Training and finetuning time
  Deep learning libraries and quality of the code
How does the approach perform on different platforms?
  Is the approach a general method, or applicable on specific hardware?

## Slide 115: Training Approaches for Co-Design
1. Train from scratch
Use pretrained large DNN model
  Initialize weights for an efficient DNN model
  Knowledge distillation to an efficient DNN model
 Need to keep pretrained model
 No guarantees which approach is better (open area of research)
Complex
DNN B
(teacher)
Simple DNN (student)
softmax
softmax
Complex
DNN A
(teacher)
softmax
scores
@eems_mit)
115
class probabilities
Try to match
[Bucilu, KDD 2006],[Hinton, arXiv 2015]

## Slide 116: Flexibility & Scalability
@eems_mit)
116

## Slide 117: Many Efficient DNN Design Approaches
pruning neurons
1 C
1
S
R
1
R
S
C
Network Pruning Efficient Network Architectures
before pruning after pruning
pruning synapses
1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0
Reduce Precision
32-bit float
8-bit fixed
Binary 0
@eems_mit)
117
No guarantee that DNN algorithm designer will use a given approach.
Need flexible DNN processor!
[Chen, SysML 2018]

## Slide 118: Limitations of Existing DNN Processors
Specialized DNN processors often rely on certain properties of the DNN model in order to achieve high energy-efficiency
Example: Reduce memory access by amortizing across PE array
PE array
Weight Memory
Activation Memory
Weight reuse
Activation reuse
@eems_mit)
118

## Slide 119: Limitations of Existing DNN Processors
PE array (spatial accumulation)
Number of filters (output channels)
Number of input channels
PE array (temporal accumulation)
Number of filters (output channels)
feature map or batch size
1
1
@eems_mit)
119
1 C
R
Reuse depends on # of channels, feature map/batch size
  Not efficient across all DNN models (e.g., efficient network architectures)
Example mapping for
Depth-wise layer
S

## Slide 120: Need Flexible Dataflow
Use flexible dataflow (Row Stationary) to exploit reuse in any dimension of DNN to increase energy efficiency and array utilization
Example: Depth-wise layer
@eems_mit)
120

## Slide 121: Need Flexible On-Chip Network for Varying Reuse
Global Buffer
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE PE PE
PE
PE
PE
PE
Global Buffer
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Global Buffer
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Global Buffer
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
When reuse available, need multicast to exploit spatial data reuse for energy efficiency and high array utilization
When reuse not available, need unicast for high BW for weights for FC and weights & activations for high PE utilization
An all-to-all on-chip network satisfies above but too expensive and not scalable
High Bandwidth, Low Spatial Reuse Low Bandwidth, High Spatial Reuse
PE PE PE PE
1D Multicast Networks
@eems_mit)
121
PE PE PE PE
Broadcast Network
[Chen, JETCAS 2019]
Unicast Networks
1D Systolic Networks

## Slide 122: Hierarchical Mesh
GLB
Cluster
Router Cluster
PE
Cluster
…
…
…
…
…
…
…
Mesh Network
All-to-all Network
High Bandwidth
@eems_mit)
122
High Reuse
Grouped Multicast
Interleaved Multicast
All-to-All
Mesh
[Chen, JETCAS 2019]

## Slide 123: Eyeriss v2: Balancing Flexibility and Efficiency
Efficiently supports
Wide range of filter shapes
  Large and Compact
Different Layers
  CONV, FC, depth wise, etc.
Wide range of sparsity
  Dense and Sparse
Scalable architecture
Over an order of magnitude faster and more energy efficient than Eyeriss v1
Speed up over Eyeriss v1 scales with number of PEs
# of PEs | 256 | 1024 | 16384
AlexNet | 17.9x | 71.5x | 1086.7x
GoogLeNet | 10.4x | 37.8x | 448.8x
MobileNet | 15.7x | 57.9x | 873.0x
12.6
10.9
5.6
@eems_mit)
123
[Chen, JETCAS 2019]

## Slide 124: Design Considerations for Flexibility and Scalability
@eems_mit)
124
Many of the existing DNN processors rely on certain properties of the DNN model
  Properties cannot be guaranteed as the wide range techniques used for efficient DNN model design has resulted in a more diverse set of DNNs
  DNN processors should be sufficiently flexible to efficiently support a wide range of techniques
Evaluate DNN processors on a comprehensive set of benchmarks
  MLPerf benchmark is a start, but may need more (e.g., reduced precision, sparsity, efficient network architectures)
Evaluate improvement in performance as resources scales up!
  Multiple chips modules [Zimmer, VLSI 2019] and Wafer Scale [Lie, HotChips 2019]

## Slide 125: Design Considerations for ASIC
@eems_mit)
125
Increase PE utilization
  Flexible mapping and on-chip network for different DNN models 
requires additional hardware
Reduce data movement
  Custom memory hierarchy and dataflows that exploit data reuse
  Apply compression to exploit redundancy in data  requires additional hardware
Reduce time and energy per MAC
  Reduce precision  if precision varies, requires additional hardware; impact on accuracy
Reduce unnecessary MACs
  Exploit sparsity  requires additional hardware; impact on accuracy
  Exploit redundant operations  requires additional hardware

## Slide 126: Other Platforms
@eems_mit)
126

## Slide 127: Processing In Memory / In Memory Compute
 Reduce data movement by moving compute into memory
Analog compute
  Increased sensitivity to circuit non- idealities: non-linearities, process, voltage, and temperature variations
V1
G1
I1 = V1×G1
V2
G2
I2 = V2×G2
I = I1 + I2
= V1×G1 + V2×G
2
Image Source: [Shafiee, ISCA 2016]
Activation is input voltage (Vi) Weight is resistor conductance (Gi)
Partial sum is output current
eNVM:[Yu, PIEEE 2018], SRAM:[Verma, SSCS 2019]
More details in tutorial @ ISSCC 2020
@eems_mit)
127

## Slide 128: Field Programmable Gate Array (FPGA)
Often implemented as matrix-vector multiply
  e.g., Microsoft Brainwave NPU [Fowers, ISCA 2018]
A popular approach uses weight stationary dataflow and stores all weights on FPGA for low latency (batch size of 1)
Reduced precision to fit more weights and MACs on FPGA
More details in tutorial @ ISSCC 2020
@eems_mit)
128

## Slide 129: DNN Processor Evaluation Tools
Require systematic way to
  Evaluate and compare wide range of DNN processor designs
  Rapidly explore design space
Accelergy [Wu, ICCAD 2019]
  Early stage energy estimation tool at the architecture level
    Estimate energy consumption based on architecture level components (e.g.,
# of PEs, memory size, on-chip network)
  Evaluate architecture level energy impact of emerging devices
    Plug-ins for different technologies
Timeloop [Parashar, ISPASS 2019]
  DNN mapping tool
  Performance Simulator  Action counts
Open-source code available at: http://accelergy.mit.edu
Accelergy
(Energy Estimator Tool)
Architecture description
Action
coAucntitosn
counts
Compound component description
…
Energy estimation
Energy estimation plug-in 0
Energy estimation plug-in 1
Timeloop
(DNN Mapping Tool & Performance Simulator)
@eems_mit)
129

## Slide 130: DNN Compilers for Diverse DNN Platforms
https://github.com/pytorch/glow
https://tvm.apache.org/
@eems_mit)
130
Compilers generate optimized code for various DNN platforms (backends) from high-level frameworks

## Slide 131: Summary
@eems_mit)
131
DNNs are a critical component in the AI revolution, delivering record breaking accuracy on many important AI tasks for a wide range of applications; however, it comes at the cost of high computational complexity
Efficient processing of DNNs is an important area of research with many promising opportunities for innovation at various levels of hardware design, including algorithm co-design
When considering different DNN solutions it is important to evaluate with the appropriate workload in term of both input and model, and recognize that they are evolving rapidly
It is important to consider a comprehensive set of metrics when evaluating different DNN solutions: accuracy, throughput, latency, power, energy, flexibility, scalability and cost

## Slide 132: Additional Resources
V. Sze, Y.-H. Chen, T-J. Yang, J. Emer, “Efficient Processing of Deep Neural Networks:
A Tutorial and Survey,” Proceedings of the IEEE, Dec. 2017
Book Coming Soon!
MIT Professional Education Course on
“Designing Efficient Deep Learning Systems”
http://professional-education.mit.edu/deeplearning
For updates
EEMS Mailing List
@eems_mit)
132
DNN tutorial website http://eyeriss.mit.edu/tutorial.html
More info about our research on efficient computing for DNNs, robotics, and health care http://sze.mit.edu

## Slide 133: References (1 of 4)
@eems_mit)
133
Deep Learning Overview
Transformer: Vaswani et al, “Attention is all you need,” NeurIPS 2017
LeNet: LeCun, Yann, et al. “Gradient-based learning applied to document recognition,” Proc. IEEE 1998
AlexNet: Krizhevsky et al. “Imagenet classification with deep convolutional neural networks,” NeurIPS 2012
VGGNet: Simonyan et al.. “Very deep convolutional networks for large-scale image recognition,” ICLR 2015
GoogleNet: Szegedy et al. “Going deeper with convolutions,” CVPR 2015
ResNet: He et al. “Deep residual learning for image recognition,” CVPR 2016
EfficientNet: Tan et al., “EfficientNet: Rethinking Model Scaling for Convolutional Neural Networks,” ICML 2019
Key Metrics and Design Objectives
Sze et al., “Hardware for machine learning: Challenges and opportunities,” CICC 2017, https://www.youtube.com/watch?v=8Qa0E1jdkrE&feature=youtu.be
Sze et al., “Efficient processing of deep neural networks: A tutorial and survey,” Proc. IEEE 2017
Williams et al., “Roofline: An insightful visual performance model for floating-point programs and multicore architectures,” CACM 2009
Chen et al., Eyexam, https://arxiv.org/abs/1807.07928
CPU and GPU Platforms
Mathieu et al., “Fast training of convolutional networks through FFTs,” ICLR 2014
Cong et al., “Minimizing computation in convolutional neural networks,” ICANN 2014
Lavin et al., “Fast algorithms for convolutional neural networks,” CVPR 2016

## Slide 134: References (2 of 4)
Specialized / Domain-Specific Hardware (ASICs): Efficient Dataflows
Chen et al., “Eyeriss: A Spatial Architecture for Energy-Efficient Dataflow for Convolutional Neural Networks,” ISCA 2016
Jouppi et al., “In-datacenter performance analysis of a tensor processing unit,” ISCA 2017
NVDLA, http://nvdla.org
Moons et al., “A 0.3–2.6 TOPS/W precision-scalable processor for real-time large-scale ConvNets,” VLSI 2017
Parashar et al, “Scnn: An accelerator for compressed-sparse convolutional neural networks,” ISCA 2017
Chen et al., “Eyeriss: An energy-efficient reconfigurable accelerator for deep convolutional neural networks,” ISSCC 2016, http://eyeriss.mit.edu
Suleiman et al., “Towards Closing the Energy Gap Between HOG and CNN Features for Embedded Vision,” ISCAS 2017
Suleiman et al., “A 58.6mW Real-time Programmable Object Detection with Multi-Scale Multi-Object Support Using Deformable Parts Models on 1920×1080 Video at 30fps,” VLSI 2016
Co-Design: Reduced Precision
Courbariaux et al., “Binaryconnect: Training deep neural networks with binary weights during propagations,” NeurIPS 2015
Li et al., “Ternary weight networks,” NeurIPS Workshop 2016
Rategari et al., “XNOR-Net: ImageNet Classification Using Binary Convolutional Neural Networks,” ECCV 2016
Lee et al., “LogNet: Energy-efficient neural networks using logarithmic computation,” ICASSP 2017
Camus et al., “Review and Benchmarking of Precision-Scalable Multiply-Accumulate Unit Architectures for Embedded Neural-Network Processing,” JETCAS 2019
@eems_mit)
134

## Slide 135: References (3 of 4)
@eems_mit)
135
Co-Design: Sparsity
Lecun et al., Optimal Brain Damage,” NeurIPS 1990
Han et al., “Learning both weights and connections for efficient neural networks,” NeurIPS 2015
Albericio et al., “Cnvlutin: Ineffectual-neuron-free deep neural network computing”, ISCA 2016
Co-Design: Efficient Network Architectures
Howard et al., “Mobilenets: Efficient convolutional neural networks for mobile vision applications”, arXiv 2017
Zhang et al., “ShuffleNet: An Extremely Efficient Convolutional Neural Network for Mobile Devices,” CVPR 2018
Lin et al., “Network in network” ICLR 2014
Huang et al., “Densely Connected Convolutional Networks,” CVPR 2017
Yu et al., “Deep layer aggregation," CVPR 2018
Zoph at al., “Learning Transferable Architectures for Scalable Image Recognition,” CVPR 2018
Co-Design: Hardware in the Loop
Yang et al., “Designing Energy-Efficient Convolutional Neural Networks using Energy-Aware Pruning,” CVPR 2017, http://eyeriss.mit.edu/energy.html
Yang et al., “NetAdapt: Platform-Aware Neural Network Adaptation for Mobile Applications,” ECCV 2018, http://netadapt.mit.edu

## Slide 136: References (4 of 4)
@eems_mit)
136
Specialized Hardware (ASICs): Flexibility and Scalability
Chen et al., “Understanding the Limitations of Existing Energy-Efficient Design Approaches for Deep Neural Networks,” SysML 2018, https://www.youtube.com/watch?v=XCdy5egmvaU
Chen et al., “Eyeriss v2: A Flexible Accelerator for Emerging Deep Neural Networks on Mobile Devices,” JETCAS 2019
Zimmer et al., “A 0.11pJ/Op, 0.32-128 TOPS, Scalable Multi-Chip-Module-based Deep Neural Network Accelerator with Ground-Reference Signaling in 16nm,” VLSI 2019
Lie (Cerebras), “Wafer Scale Deep Learning,” Hot Chips 2019
Other Platforms: Processing In Memory / In-Memory Computing and FPGAs
Sze et al., “How to Understand and Evaluate Deep Learning Processors,” ISSCC Tutorial 2020, http://isscc.org/
Verma et al., “In-Memory Computing: Advances and prospects,” ISSCC Tutorial 2018 / SSCS Magazine 2019
Yu, “Neuro-Inspired Computing with Emerging Nonvolatile Memorys,” Proc. IEEE 2018
Yang et al., “Design Considerations for Efficient Deep Neural Networks on Processing-in-Memory Accelerators,” IEDM 2019
Fowers et al., “A configurable cloud-scale DNN processor for real-time AI,” ISCA 2018
DNN Processor Evaluation Tools
Wu et al., “Accelergy: An Architecture-Level Energy Estimation Methodology for Accelerator Designs,” ICCAD 2019, http://accelergy.mit.edu
Parashar et al., “Timeloop: A Systematic Approach to DNN Accelerator Evaluation,” ISPASS 2019

## Slide 137: NetAdapt: Problem Formulation
max 𝐴𝑐𝑐 𝑛𝑒𝑡 𝑠𝑢𝑏/𝑒𝑐𝑡 𝑡𝑜 𝑅𝑒𝑠2 𝑛𝑒𝑡 ≤ 𝐵𝑢𝑑2, / = 1, ⋯ , 𝑚
𝑛𝑒𝑡
Break into a set of simpler problems and solve iteratively
max 𝐴𝑐𝑐 𝑛𝑒𝑡< 𝑠𝑢𝑏/𝑒𝑐𝑡 𝑡𝑜 𝑅𝑒𝑠2 𝑛𝑒𝑡< ≤ 𝑅𝑒𝑠2 𝑛𝑒𝑡<=> − ∆𝑅<,2, / = 1, ⋯ , 𝑚
𝑛𝑒𝑡;
*Acc: accuracy function, Res: resource evaluation function,
ΔR: resource reduction, Bud: given budget
Advantages
  Supports multiple resource budgets at the same time
  Guarantees that the budgets will be satisfied because the resource consumption decreases monotonically
  Generates a family of networks (from each iteration) with different resource versus accuracy trade-offs
@eems_mit)
137

## Slide 138: NetAdapt: Simplified Example of One Iteration
Code available at http://netadapt.mit.edu
Latency: 100ms Budget: 80ms
100ms 90ms
80ms
100ms
80ms
Selected
Selected
2. Meet Budget
Layer 1
Layer 4
…
Acc: 60%
Acc: 40%
…
Selected
Latency: 80ms Budget: 60ms
1. Input
3. Maximize 4. Output Accuracy
Network from Previous Iteration
@eems_mit)
138
Network for Next Iteration